## Slide 1
Picture Manipulation using Hardware
Presents by- Uri Tsipin & Ran Mizrahi
Supervisor– Moshe Porian
Middle presentation
Dual-semester project
29.1.2012

## Slide 2: Agenda
Intro – Problem, Project’s goals, Algorithm
Previous System – Explained
Degeneration of the system
New Top Architecture – Additions and modifications
Data Flow
Simulations
Missions ahead + Time Table

## Slide 3: Intro
Many military and civilian application use image manipulation as an integral part of their function
Helmet mounted displays
Medical procedures
Army surveillance gear

## Slide 4: Problem
Image Processing algorithms such as:
Image Rotation
Zoom
Crop Image
which implemented by software are:
Slow
Heavy power consumers
Large space consumers
Solution
Hardware implementation of the algorithms
using Board with FPGA and External Memory

## Slide 5: Project’s Goals
Implement the following algorithms using FPGA:
Full panoramic rotation: 0 to 360 degrees
Support of Zoom function
Support of Crop-Image function
Minimum image distortion

## Slide 7: Top Architecture – Previous System
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Notes: ארכיטקטורה מפרויקט של סטודנטים מהפקולטה משנה שעברה.
המערכת לוקחת תמונה דחוסה שמקודדת בRUNLENGTH (מה שלא ייקרה אצלנו)
כותבת אותה דחוסה לתוך הזכרון
קוראת אותה מהזכרון , פורסת אותה ומציגה אותה למסך.

## Slide 8: Degeneration of the system
1. Editing the Matlab GUI to support non compressed image
Old Uart Message
Header
Tail
New Uart Message
Data : Gray level + repetitions
Gray Level
Repetition
Data
Notes: לפני השינוי מערכת המטלב דחסה תמונה בקידוד runlength
לאחר מכן חלקה את החבילה למנות על מנת לשלוח אותה בUART
אצלנו במערכת, התמונה אינה עוברת דחיסה, כמו כן נוספה תמיכה של כתיבה פרמטרי משתמש אל הרגיסטרים המתאימים.
עדכון חישובי הCRC.

## Slide 9: Degeneration of the system
2. Changes that were made in Display Block
  Removal of Runlen Extractor (Decompressor)
  Update of Processes in Pixel Manager
Decompressor
FIFO
VESA
Ctrl.
req_ln_trig
& Pixels, VSync
Pixel Manager
(Req for Data)
WBM
MUX
Synthetic
Pic. Gen
Dual Clk FIFO
8 bit
8 bit
Hsync,
VSync
Display Controller
WBS
4
- 133 MHz
- 40 MHz
Notes: פיקסל מנג'ר אחראי לקרוא למידע מהזכרון החיצוני לטובת התצוגה
עד עשתה הוא ביקש מידע שכלל גוון אפור+מספר חזרות וכך ספר את מספר הפיקבלים הדרושים על מנת להרכיב תמונה בצג
אנחנו עדכנו אותו על מנת שיתמוך בDATA שאינו מכיל מספרי חזרות – עדכוני קאונטרים

## Slide 10: Degeneration of the system
3. Changes in Top Design & Top TB
  Changes to support different image resolutions
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
VESA
Wishbone
INTERCON
Notes: לצורך סימולציה של תמונה לא דחוסה, נדרש הרבה זמן
לכן העדפנו לעבוד על רזולוציות נמוכות. לקח הרבה זמן כדי לגרום למערכת לתמוך ברזולוציות קטנות
שינוי ג'נריקים, הרבה דיבאגים ולמידה של המערכת

## Slide 11: Top Architecture – New
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Image Manipulation
WBS
WBM

## Slide 12: Image Manipulation – New Block (Prototype)
Parameter registers- holds user parameters (angle,zoom,crop)
Address Calculator – Calculates "matrix address" of 4 pixels that are required for the bilinear-interpolation
Address Converter – Converts a "matrix address" into a 1D SDRAM address
Bilinear Interpolator – Calculates a mean average between 4 pixels
WBM
F
Addr Converter
Biliniar Interpulation
Addr Calculator
WBS
6
Image Manipulation
Param Reg
Notes: על מנת לסובב תמונה נדרשים 4 פקסלים מתמונת המקור.
כל פיקסל נקרא בנפרד – תחילה מחושבת הכתובת המטריצית של הפיקסל הדרוש (מתוך הארבעה)
לאחר מכן הכתובת מומרת לכתובת SDRAM (יכול להיות ששני הרכיבים יאוחדו לרכיב אחד)
לאחר מכן מתבצעת קריאה מהזכרון של ערך הפקסל,
חוזר על עצמו 4 פעמים עד אשר יש לנו ארבעה פקסלים לביצוע אינטרפולציה בי-לינארית
מבוצעת אינטרפולציה וערך הפיקסל החדש נכתב לבנק חדש בזכרון שיכיל את התמונה המסובבת

## Slide 13: Data Flow - Ilustration
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Image Manipulation
WBS
WBM
Notes: תרשים זרימת מידע

## Slide 14: Parameter Registers
New registers were added to the system in order to hold the user parameters, which are required for image manipulation.
Registers addresses were expanded to 5bit addresses (up-to 32 registers)
Register's name | Address (hex) | Size (bytes) | Purpose | Place
Angle_reg | C-D | 2 | Holds rotation angle (degrees) | Img_man_top
X_start_reg | E-F | 2 | Holds Xstart | Img_man_top
Y_start_reg | 10-11 | 2 | Holds Ystart | Img_man_top
zoom_reg | 12-13 | 2 | Holds Zoom Factor | Img_man_top

## Slide 15: Parameter Registers - Simulation

## Slide 16: Data Flow - Simulation
Rx-Path to Memory Mang.
Memory Mang. To SD-RAM
Data
VESA Out

## Slide 17: Testability & GUI
Input Param.

## Slide 18: Problems during the process
Making the system support low resolutions:
  Debugging the current system in order to learn the data flow, components, processes.
  Changing generics in code
Making the system support non compressed image
  Removal unnecessary components
  Change the matlab output.

## Slide 19: Missions ahead
Burn current system (without image manipulation) to FPGA
Create image manipulation block
Test and debugging

## Slide 20: Time Table - 2012
Tasks | Week
Exams period | February
VHDL implementation of Image manipulation block | March
Simulations and Debugging | April
Synthesis, 2nd Presentation | May
Integration and Lab testing | June
Final Presentation | July