## Slide 1
Picture Manipulation using Hardware
Presents by- Uri Tsipin & Ran Mizrahi
Supervisor– Moshe Porian
Characterization presentation
Dual-semester project
24.11.2011

## Slide 2: Agenda
Introduction
Project’s Goals
Algorithm
  Image rotation
  Zoom
  Crop
Project Requirements
Top Architecture (reuse from previous project)
Optional solutions
Testability & GUI
Time table

## Slide 3: Intro
Many military and civilian application use image manipulation as an integral part of their function
Helmet mounted displays
Medical procedures
Army surveillance gear

## Slide 4: Problem
Image Processing algorithms such as:
Image Rotation
Zoom
Crop Image
which implemented by software are:
Slow
Heavy power consumers
Large space consumers

## Slide 5: Solution
Hardware implementation of the algorithms
using Board with FPGA and External Memory

## Slide 6: Project’s Goals
Implement the following algorithms using FPGA:
Full panoramic rotation: 0 to 360 degrees
Support of Zoom function
Support of Crop-Image function
Minimum image distortion

## Slide 7: Algorithm
Crop – user defined region of interest
Rotate/Zoom - Run a nested loop (over all pixels)
  Rotated pixel is estimated using bi-linear interpolation
  Zoom is achieved using scale factor
Notes: חיתוך תמונה – שתי אופציות למימוש: 1. חיתוך כבר בשלב קבלת הנתוניתם, ז"א לכתוב לראם רק את החלק הרלוונטי 2. העתקת התמונה בשלמותה אל הRAM ועבודה על התחום עניין )ROI(
סיבוב וזום – יוסבר בשקפים הבאים.

## Slide 8: Algorithm – Image Rotation
(X,Y)
R1
R2
Output
Source
Y’
X’
Y
X
Bi-Linear
Notes: שקף שמסביר את תהליך סיבוב התמונה
רעיון עיקרי – עובדים על פיקסלים בתמונת היעד ומשערכים את ערכם מתמונת המקור
א. עוברים על כל פיקסל בתמונת היעד
ב. משערכים את הכתובת שלו בתמונת המקור
ג. עושים אינטרפולציה בי-לינארית של 4 השכנים שלו, ז"א ממוצע משוקלל

## Slide 9: Algorithm - Zoom
Centered Zoom – the reference point for zoom is the center of the image

## Slide 10: Algorithm - Crop
Input image
Output image
(x_start,y_start)
The user may define a region of interest (ROI)

## Slide 11: Project’s requirements
Input monochromatic image with resolution of 600x800
Output resolution 480x640 with user defined region of interest
Centered Zoom, where zoom factor must be greater than 1
Minimum image distortion
Input freq. 50MHz
Main clock 133MHZ
VESA (monitor) freq. 40 MHz

## Slide 12: Top Architecture- Reused
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Display
Controller
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
WBM
UART
UART
VESA
Wishbone
INTERCON
FPGA
Notes: ארכיטקטורה מפרויקט של סטודנטים מהפקולטה משנה שעברה.
המערכת לוקחת תמונה דחוסה שמקודדת בRUNLENGTH (מה שלא ייקרה אצלנו)
כותבת אותה דחוסה לתוך הזכרון
קוראת אותה מהזכרון , פורסת אותה ומציגה אותה למסך.

## Slide 13: Solution 1 – rotation during reading from memory
Write original image to the SDRAM
Rotate image while reading the image into the display
Notes: - כותבים את התמונה המקורית לזכרון
- תוך כדי קריאה לצג, מסובבים את התמונה

## Slide 14: Solution 1 – rotation during reading from memory
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Display
Controller
WBS
Wishbone
INTERCON
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
WBM
UART
UART
VESA

## Slide 15: Solution 1 – Pros & Cons
Good image quality
Reading rate issue– frame writing rate to VESA vs. frame reading rate from SDRAM
Works good on small images and small region of interest
Notes: הבעיה שהתעוררה היא נושא קצב הקריאה מה-SDRAM לעומת הכתיבה ל- VESA.
קצב העברת הנתונים של הVESA יותר מהיר מהקצב שהSDRAM מספק שורות. הוא צריך יותר שורות ממה שהSDRAM מסוגל לספק לו.
ניתן לנסות לעבוד מראש עם תמונה קטנה יותר משמעותית גם בכניסה ב UART וגם בתוצר לVESA.
לאחר שנראה שהכל עובד ננסה לבצע אופטימיזציות ובחינת עמידה ב troughput הרצוי.

## Slide 16: Solution 2 – Assigning values to destination
Rotate Image while receiving it through UART
Rotated Image is written to SDRAM

## Slide 17: Solution 2 – Source to destination mapping
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Display
Controller
WBS
Wishbone
INTERCON
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
WBM
UART
UART
VESA

## Slide 18: Solution 2 – Pros & Cons
Simpler to implement
Assigning values to destination causes distortion in the images

## Slide 19: Solution 3 – Image processing using the SDRAM (selected solution)
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Display
Controller
WBS
Wishbone
INTERCON
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
WBM
UART
UART
VESA

## Slide 20: Solution 3 – Inside the SDRAM
1.Divide the memory into 3 parts
2.Receive and store first image
3.Read from the memory, rotate image and store it in the memory
4.Receive and store new image and push rotated image to display
And so on…

## Slide 21: Solution 3 – Image processing using the SDRAM (selected solution)
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Display
Controller
WBS
Wishbone
INTERCON
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
WBM
UART
UART
VESA

## Slide 22: Solution 3 – Pros & Cons
Good Image quality using destination from source mapping
Work on all image sizes (according to project requirements)
Harder to implement
Intervention in memory management block might be needed
Notes: ממפים את היעד מתוך המקור

## Slide 23: Testability & GUI

## Slide 24: Time Table
Tasks | Week
Project Characterization & learning the work environments | 1-4
Initial Algorithm and testing using Matlab | 
Characterization presentation | 
Full Characterization of all blocks | 5-6
VHDL implementation of main blocks (memory management, rotation, zoom etc.) | 7-11
Mid Simulation | 12
Simulations | 12-13
Final presentation (part A) | 14
Part B – Synthesis, building GUI, Integration and Lab testing