## Slide 1
Picture Manipulation using Hardware
Presents by- Uri Tsipin & Ran Mizrahi
Supervisor– Moshe Porian
Final Presentation – Part B
Dual-semester project
10.06.2013

## Slide 2: Agenda
Intro – Problem, Project’s goals, Algorithm
Previous System – Explained
New Top Architecture – Additions and modifications
µArchitucture- components description, simulations and testing
GUI
Testing
Problems during the project
Conclusions

## Slide 3: Intro
Many military and civilian application use image manipulation as an integral part of their function
Helmet mounted displays
Medical procedures
Army surveillance gear

## Slide 4: Problem
Image Processing algorithms such as:
Image Rotation
Zoom
Crop Image
which implemented by software are:
Slow
Heavy power consumers
Large space consumers
Solution
Hardware implementation of the algorithms
using Board with FPGA and External Memory

## Slide 5: Project’s Goals
Implement the following algorithms using FPGA:
Full panoramic rotation: 0 to 360 degrees
Support of Zoom function
Support of Crop-Image function
Minimum image distortion

## Slide 6
(x_start,y_start)
Input image
Notes: Zoom – ככל הנראה ימומש עבור חזקות של 2 ז"א 2,4,8
Crop – המשתמש יתן קורדיטת עניין שמתארת את הפינה העליונה של התחום עניין
כרגע כל האלגוריתמים ממומשים בתוך החישוב של הכתובת של פיקסל השערוך,
אנחנו עדיין צריכים לבדוק אם המימוש החומרתי של הסיפור יבוצע בדיוק באותו האופן

## Slide 7: Top Architecture – Previous System
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Notes: ארכיטקטורה מפרויקט של סטודנטים מהפקולטה משנה שעברה.
המערכת לוקחת תמונה דחוסה שמקודדת בRUNLENGTH (מה שלא ייקרה אצלנו)
כותבת אותה דחוסה לתוך הזכרון
קוראת אותה מהזכרון , פורסת אותה ומציגה אותה למסך.

## Slide 8: Problems during the process
Making the system support low resolutions:
  Debugging the current system in order to learn the data flow, components, processes.
  Changing generics in code
Making the system support non compressed image
  Removal unnecessary components
  Change the matlab output.

## Slide 9: Top Architecture – New
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Image Manipulation
WBS
WBM

## Slide 10: Data Flow - Ilustration
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Image Manipulation
WBS
WBM
Notes: תרשים זרימת מידע

## Slide 11: Image Manipulation – New Block
Parameter registers- holds user parameters (angle,zoom,crop)
Address Calculator – Calculates "matrix address" of 4 pixels that are required for the bilinear-interpolation and converts the "matrix address" into a 1D SDRAM address
Bilinear Interpolator – Calculates a mean average between 4 pixels
Image Manipulation Manger – Controller for the block
Internal RAM- 1 KB
WBM/WBS- top block interfaces
WBM
Image Manipulation
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE
Reg
Notes: על מנת לסובב תמונה נדרשים 4 פקסלים מתמונת המקור.
כל פיקסל נקרא בנפרד – תחילה מחושבת הכתובת המטריצית של הפיקסל הדרוש (מתוך הארבעה)
לאחר מכן הכתובת מומרת לכתובת SDRAM (יכול להיות ששני הרכיבים יאוחדו לרכיב אחד)
לאחר מכן מתבצעת קריאה מהזכרון של ערך הפקסל,
חוזר על עצמו 4 פעמים עד אשר יש לנו ארבעה פקסלים לביצוע אינטרפולציה בי-לינארית
מבוצעת אינטרפולציה וערך הפיקסל החדש נכתב לבנק חדש בזכרון שיכיל את התמונה המסובבת

## Slide 12: Parameter Registers
New registers were added to the system in order to hold the user parameters, which are required for image manipulation.
Registers addresses were expanded to 5bit addresses (up-to 32 registers)
Register's name | Address | Size (bytes) | Purpose | Place
x_start_reg | E | 2 | X crop coordinate | Img_man_top
y_start_reg | 10 | 2 | Y crop coordinate | Img_man_top
zoom_reg | 12 | 2 | Zoom ratio | Img_man_top
cos_reg | 14 | 2 | Cosine of rotation angle, multiplied by 0x100 | Img_man_top
Sin_reg | 16 | 2 | Sine of rotation angle, multiplied by 0x100 | Img_man_top
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg

## Slide 13: Address Calculator
Main Goal – Calculates "matrix address“
of 4 pixels that are required for the bilinear-interpolation.
Method - Given a current pixel index in the output image, the unit will calculate the origin addresses of the pixel, by the following formula:
Inputs:
  User parameters (zoom factor, sin/cos[angle], crop indexes)
  Row/Col index (current calculating coordinate)
Outputs:
  TL,TR,BL,BR coordinate address
  Delta Row, Delta Col- holds the weight for billinear interpolation.
  Out of range
  Valid,Finish
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg

## Slide 14: Addr. Calc. - Improved µArchitucture
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg

## Slide 15: Addr. Calc. – working with fractures
Zoom=x4
Angle =60 deg
X Start =30
Y Start =29
Zoom_factor=(1/zoom)*128=32
Angle =cos(60)=0.5*128=64 X/Y Start – remain the Same, no fracture required
Requested decimal accuracy – 2 digits [0-0.99]
in order to work with std_logic_signals(binary) (fixed/float types experience synthesis problems)
all signals were multiplied by 2^7=128 (2^6=64-> not enough accuracy)
Example (user param.)
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager
x128

## Slide 16: Bilinear Interpolator
Main Goal – Calculates the mean average of 4 given gray-scale values.
Formula –
Inputs
  4 pixels, 8bit grey scale
  Weight fraction (row/col)
Outputs
  Result pixel (the mean average of the input)
  Valid signal
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg

## Slide 17: Bilinear Interpolator – µArchitucture
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg

## Slide 18: Image Manipulation Manager –(1)
Main Goal – Control the data flow within the image manipulation block and send Read/Write requests to other units using the wishbone protocol
Method – the controller is implemented via a several FSM’s.
Enable output for display
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg

## Slide 19: Image Manipulation Manager – Main Features
RAM- internal RAM which stores results before write-back to SDRAM. Burst RAM size is generic- 1024 bytes.
Top FSM- controls the data flow between inner units and the main system.
Read FSM- controls the read process, sub-phase to the top FSM.
Write FSM- controls the write process, sub-phase to the top FSM. Writes the RAM contents to SDRAM.
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg

## Slide 20: Image Manipulation Manager – Interfaces
WBM_rd- interface for read purposes.
WBM_wr- interface for write purposes.
WBS- interface for writing to parameter registers.
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg
Notes: היה צריך 2 WBM כיוון שכל אחד מהם מתחבר ל-WBS אחר ב-MEMORY דרך INTERCON שונה.
לצבוע את הבלוק הרלוונטי לפי BULLET

## Slide 21: Image Manipulation Manager - µArchitucture
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg
TOP FSM
Read FSM
Write FSM
Generic RAM
(1024 Bytes)
Coordinate Process
Address Calculator Process
Bilinear Process
ImgMan Manger

## Slide 22: Img. Man. Manager - FSM
WBM
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE Reg

## Slide 23: Test Benches
Purpose- test functionality of the IMG_MAN new block, debug problems during integration
Implementation- Matlab, text files from ModelSim

## Slide 24: Test Bench (1)- ADDR_CLAC
ModelSim generates txt file with the calculated addresses
Addr_calc_tb
Addr_calc
Output 1,1
Output.txt
1
1
2
3
Output 1,2
Output 1,3
Output 512,512
600
800
.
.
.
.

## Slide 25: Test Bench (1)- ADDR_CLAC cont.
Zoom=x4
Angle =60 deg
X Start =30
Y Start =29
Using Matlab, the output image is created

## Slide 26: Test Bench (2)- IMG_MAN
ModelSim generates txt file before/after writing back the pixels values to internal RAM, in order to make sure the new block is correct
WBM
Image Manipulation
Addr Calculator
Param Registers
WBS
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
WBM
TYPE
Reg

## Slide 27: Synthesis, P&R
Latency- time from end of transmission to end of manipulation- 435422720 ns,
or 0.4354 sec.
At 100 MHz: 43542272 cycles
System Timing Results

## Slide 28: GUI
Load image
Set Parameters
Click to transmit
Debug option – synthetic image
Expected Output
Transmission time
Make sure Transmission enabled
Select image

## Slide 29: Debugging in Lab – Synthetic Generator

## Slide 30: Lab Testing
GUI
Display
DE2
PC

## Slide 31: Debugging in Lab
Mem Type Reg
DBG MSB REG
Sine Reg
Uart Serial out

## Slide 32: Main milestones
Learn previous system
Degenerate system to project goals
Build new block, functional TB, interfaces to main system (Wishbone protocol)
Integrate the new block with main system
Lab testing and debugging

## Slide 33: Test results
333[deg] | 180[deg] | 90[deg]
zoomx1.5 | zoom x2 | Zoom x1
Start Point [1,1] | Start Point [1,1] | Start Point [200,200]

## Slide 34: Working methods
Top down design
Pipeline
Test bench
Results comparison with Matlab (Golden Model)
Components documenting
Working on lower resolution during simulations
design with generics parameters (change resolution)
Synchronize files via SVN.
Notes: התכן נעשה על ידי בחינה של המערכת הכוללת, לאחר מכן תכן של הבלוק שלנו ואז בוצע תכן לכל רכיב בתוך הבלוק
האלגוריתם כולל חיושבים אריתמטיים עם הכפלות מרובות, והיות והכפלה הינה צרכן משאבים, פיצול החישוב משפר את הקצב התוצאות
בדיקת הרכיבים נעשתה על ידי יצירת קובץ TB לכל קומפוננטה, שמטרתו לדמות כניסות אפשריות למערכת ובדיקת התוצאות
בדיקת התוצאות נעשה מול האלגוריתם שרץ בסביבת MATLAB, השוואה עם פלט ויזואלי
תיעוד לאורך התהליך עזר בבננית המצגת, מסמך הפרויקט ולשימוש חוזר בעתיד
מאפשר עבודה מנקודות קצה שונות ושחזור במקרה של באגים

## Slide 35: Problems during the process (1)
Working with fractures
First version of addr_calc used fixed point package.
Problem occurred during synthesis.
Solution- work with regular std_logic_Vector, with relevant adjustments.

## Slide 36: Problems during the process (2)
Trigonometric calculations (sine, cosine)
planed to be executed by VHD process, consumes expensive hardware resources.
Solution- calculate Cos/Sin by software (Matlab).

## Slide 37: Problems during the process (3)
Timing issues- synthesis timing results did not meet the requirements.
solution- break arithmetic calculations into parts (piping).

## Slide 38: Problems during the process (4)
Resolution issues- high resolution simulations takes more than 3 hours.
solution- working with lower resolution and diagnose the errors before high resolution simulations.

## Slide 39: Problems during the process (5)
Resolution issues- failed passing simulations while upgrade to high resolution. Even though generics were used, it was hard to detect the specific errors.
solution- update VHDL generics (on the main system-Pixel manager), update counters.

## Slide 40: Conclusions/lessons (1)
Pipeline makes the throughput shorter. With “heavy” calculations, it is recommended to break the arithmetic process.

## Slide 41: Conclusions/lessons (2)
Working with generics parameters make the design more flexible.

## Slide 42: Conclusions/lessons (3)
Top down design divides the coding procedure into stages, allows more than one person to work on solution, allows parallel work.

## Slide 43: Time Table – 2012-2013
Month | 
Project Start | November 2011
Mid Final Part A | January 2012
Final Part A | November 2012
Planed Final Part B | March 2013
Final Part B | June 2013
3 months delay