## Slide 1
Picture Manipulation using Hardware
Presents by- Uri Tsipin & Ran Mizrahi
Supervisor– Moshe Porian
Final Presentation – Part A
Dual-semester project
12.11.2012

## Slide 2: Agenda
Intro – Problem, Project’s goals, Algorithm
Previous System – Explained
Degeneration of the system
New Top Architecture – Additions and modifications
µArchitucture- components description, simulations and testing
Missions ahead + Time Table

## Slide 3: Intro
Many military and civilian application use image manipulation as an integral part of their function
Helmet mounted displays
Medical procedures
Army surveillance gear

## Slide 4: Problem
Image Processing algorithms such as:
Image Rotation
Zoom
Crop Image
which implemented by software are:
Slow
Heavy power consumers
Large space consumers
Solution
Hardware implementation of the algorithms
using Board with FPGA and External Memory

## Slide 5: Project’s Goals
Implement the following algorithms using FPGA:
Full panoramic rotation: 0 to 360 degrees
Support of Zoom function
Support of Crop-Image function
Minimum image distortion

## Slide 6
Notes: Zoom – ככל הנראה ימומש עבור חזקות של 2 ז"א 2,4,8
Crop – המשתמש יתן קורדיטת עניין שמתארת את הפינה העליונה של התחום עניין
כרגע כל האלגוריתמים ממומשים בתוך החישוב של הכתובת של פיקסל השערוך,
אנחנו עדיין צריכים לבדוק אם המימוש החומרתי של הסיפור יבוצע בדיוק באותו האופן

## Slide 7: Top Architecture – Previous System
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Notes: ארכיטקטורה מפרויקט של סטודנטים מהפקולטה משנה שעברה.
המערכת לוקחת תמונה דחוסה שמקודדת בRUNLENGTH (מה שלא ייקרה אצלנו)
כותבת אותה דחוסה לתוך הזכרון
קוראת אותה מהזכרון , פורסת אותה ומציגה אותה למסך.

## Slide 8: Degeneration of the system
1. Editing the Matlab GUI to support non compressed image
Old Uart Message
Header
Tail
New Uart Message
Data : Gray level + repetitions
Gray Level
Repetition
Data
Notes: לפני השינוי מערכת המטלב דחסה תמונה בקידוד runlength
לאחר מכן חלקה את החבילה למנות על מנת לשלוח אותה בUART
אצלנו במערכת, התמונה אינה עוברת דחיסה, כמו כן נוספה תמיכה של כתיבה פרמטרי משתמש אל הרגיסטרים המתאימים.
עדכון חישובי הCRC.

## Slide 9: Degeneration of the system
2. Changes that were made in Display Block
  Removal of Runlen Extractor (Decompressor)
  Update of Processes in Pixel Manager
Decompressor
FIFO
VESA
Ctrl.
req_ln_trig
& Pixels, VSync
Pixel Manager
(Req for Data)
WBM
MUX
Synthetic
Pic. Gen
Dual Clk FIFO
8 bit
8 bit
Hsync,
VSync
Display Controller
WBS
4
- 133 MHz
- 40 MHz
Notes: פיקסל מנג'ר אחראי לקרוא למידע מהזכרון החיצוני לטובת התצוגה
עד עשתה הוא ביקש מידע שכלל גוון אפור+מספר חזרות וכך ספר את מספר הפיקבלים הדרושים על מנת להרכיב תמונה בצג
אנחנו עדכנו אותו על מנת שיתמוך בDATA שאינו מכיל מספרי חזרות – עדכוני קאונטרים

## Slide 10: Degeneration of the system
3. Changes in Top Design & Top TB
  Changes to support different image resolutions
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
VESA
Wishbone
INTERCON
Notes: לצורך סימולציה של תמונה לא דחוסה בגודל מלא (640x480 על פי דרישות הפרויקט), נדרש הרבה זמן
לכן העדפנו לעבוד על רזולוציות נמוכות. לקח הרבה זמן כדי לגרום למערכת לתמוך ברזולוציות קטנות
שינוי ג'נריקים, הרבה דיבאגים ולמידה של המערכת

## Slide 11: Problems during the process
Making the system support low resolutions:
  Debugging the current system in order to learn the data flow, components, processes.
  Changing generics in code
Making the system support non compressed image
  Removal unnecessary components
  Change the matlab output.

## Slide 12: Top Architecture – New
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Image Manipulation
WBS
WBM

## Slide 13: Data Flow - Ilustration
TX Path
Memory
Management
RX Path
SDRAM Controller
WBS
WBS
WBM
WBM
WBS
WBS
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
WBM
Display
Controller
WBS
WBM
UART
UART
VESA
Wishbone
INTERCON
Image Manipulation
WBS
WBM
Notes: תרשים זרימת מידע

## Slide 14: Image Manipulation – New Block
Parameter registers- holds user parameters (angle,zoom,crop)
Address Calculator – Calculates "matrix address" of 4 pixels that are required for the bilinear-interpolation and converts the "matrix address" into a 1D SDRAM address
Bilinear Interpolator – Calculates a mean average between 4 pixels
Image Manipulation Manger – Controller for the block
WBM
F
Biliniar Interpolation
Addr Calculator
WBS
6
Image Manipulation
Param Reg
Img_man_manager
Notes: על מנת לסובב תמונה נדרשים 4 פקסלים מתמונת המקור.
כל פיקסל נקרא בנפרד – תחילה מחושבת הכתובת המטריצית של הפיקסל הדרוש (מתוך הארבעה)
לאחר מכן הכתובת מומרת לכתובת SDRAM (יכול להיות ששני הרכיבים יאוחדו לרכיב אחד)
לאחר מכן מתבצעת קריאה מהזכרון של ערך הפקסל,
חוזר על עצמו 4 פעמים עד אשר יש לנו ארבעה פקסלים לביצוע אינטרפולציה בי-לינארית
מבוצעת אינטרפולציה וערך הפיקסל החדש נכתב לבנק חדש בזכרון שיכיל את התמונה המסובבת

## Slide 15: Parameter Registers
New registers were added to the system in order to hold the user parameters, which are required for image manipulation.
Registers addresses were expanded to 5bit addresses (up-to 32 registers)
Register's name | Address | Size (bytes) | Purpose | Place
x_start_reg | E | 2 | X crop coordinate | Img_man_top
y_start_reg | 10 | 2 | Y crop coordinate | Img_man_top
zoom_reg | 12 | 2 | Zoom ratio | Img_man_top
cos_reg | 14 | 2 | Cosine of rotation angle, multiplied by 0x100 | Img_man_top
Sin_reg | 16 | 2 | Sine of rotation angle, multiplied by 0x100 | Img_man_top
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 16: Parameter Registers – Simulation
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager
Notes: כתיבה לרגיסטר של פרמטרי משתמש-
הרגיסטרים יושבים בטופ של הבלוק
הכתיבה נעשית מהתוכנה, כלומר בGUI המשתמש מכניס את הפרמטרים שלו, ואז הMATLAB עוטף אותם בחבילה שנשלחת דרך הUART ומפוענחת בRX ומשם מנותבת אל היעד שלה.

## Slide 17: Address Calculator
Main Goal – Calculates "matrix address" of 4 pixels that are required for the bilinear-interpolation.
Method - Given a current pixel index in the output image, the unit will calculate the origin addresses of the pixel, by the following formula:
Inputs:
  User parameters (zoom factor, sin/cos[angle], crop indexes)
  Row/Col index (current calculating coordinate)
Outputs:
  TL,TR,BL,BR coordinate address
  Delta Row, Delta Col- holds the weight for billinear interpolation.
  Out of range
  Valid,Finish
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 18: Addr. Calc. - Initial µArchitucture
Synthesis Results:
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager
Incompliant with frequency requirements

## Slide 19: Addr. Calc. - Improved µArchitucture
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 20: Addr. Calc. – working with fractures
Zoom=x4
Angle =60 deg
X Start =30
Y Start =29
Zoom_factor=(1/zoom)*128=32
Angle =cos(60)=0.5*128=64 X/Y Start – remain the Same, no fracture required
Requested decimal accuracy – 2 digits [0-0.99]
in order to work with std_logic_signals(binary) (fixed/float types experience synthesis problems)
all signals were multiplied by 2^7=128 (2^6=64-> not enough accuracy)
Example (user param.)
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager
x128

## Slide 21: Addr. Calc.– first valid output
trigger
1st output
2nd output
latency – 12 Cycles
Throughput – 5 Cycles
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager
Notes: ניתן לראות שקצב התוצאות הוא בהתאם למספר דרגות הPIPE

## Slide 22: Addr. Calc.– mid valid output
output
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 23: Addr. Calc.– end of calc. process
finish
New image indexes
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 24: Addr. Calc. –Test Bench
Addr_calc_tb
Addr_calc
Output 1,1
Output.txt
1
1
2
3
Output 1,2
Output 1,3
Output 600,800
600
800
.
.
.
.
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager
Notes: הTB מייצר בעזרת לולאה כפולה אינדקסי כניסה עבור הaddr_calc (כתובות של מטריצה עבור תמונת היציאה)
הפלט של addr_calc – 4 כתובות RAM עבור כל פיקסל בתמונת היעד + 2 משקלים לאינטרפולציה ->נכתב לתוך קובץ הטקסט

## Slide 25: Addr. Calc. – Testing with Matlab
Zoom=x4
Angle =60 deg
X Start =30
Y Start =29
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager
Notes: התמונה בזיכרון אמורה לשבת כולה בכתובות רצופות מ1 והלאה, לכן לקחנו את התמונה (מערך דו-מימדי) והפכנו אותה למערך אחד ארוך – זה בעצם ממדל לנו את הזיכרון.
לאחר מכן לקחנו את קובץ הפלט של הקואורדינטות ובנינו על פיו את תמונת הפלט.
כאשר את הבי-לינאריות ביצענו על ידי המטלב כרגע ע"פ הפרמטרים (משקלי השברים) שבקובץ הטקסט
התמונה הסופית הינה כפי שהתקבלה במטלב

## Slide 26: Addr. Calc. – Various Test Results (1)
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 27: Addr. Calc. – Various Test Results(2)
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 28: Addr. Calc. – Various Test Results(3)
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 29: Addr. Calc. – Various Test Results(4)
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 30: Addr. Calc. – Various Test Results(5)
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 31: Bilinear Interpolator
Main Goal – Calculates the mean average of 4 given gray-scale values.
Formula –
Inputs
  4 pixels, 8bit grey scale
  Weight fraction (row/col)
Outputs
  Result pixel (the mean average of the input)
  Valid signal
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 32: Bilinear Interpolator – µArchitucture
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 33: Bilinear Interpolator – Simulation
trigger
inputs
Pipeline
Results
5 cycles
Matlab Results for comparison
error margin of maximum 4 grey scale levels which means 1.5% in 8 bit image
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 34: Image Manipulation Manager – (1)
Main Goal – Control the data flow within the image manipulation block and send read write requests to outer units using the wishbone protocol
Method – the controller is implemented via a several FSM’s.
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 35: Image Manipulation Manager – Main משהו
RAM- internal RAM which stores results before write-back to SDRAM. Burst RAM size is generic- 1024 bytes.
Top FSM- controls the data flow between inner units and the main system.
Read FSM- controls the read process, sub-phase to the top FSM.
Write FSM- controls the write process, sub-phase to the top FSM. Writes the RAM contents to SDRAM.
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 36: Image Manipulation Manager – interfaces
WBM_rd- interface for read purposes.
WBM_wr- interface for write purposes.
WBS- interface for writing to parameter registers.
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager
Notes: היה צריך 2 WBM כיוון שכל אחד מהם מתחבר ל-WBS אחר ב-MEMORY דרך INTERCON שונה.
לצבוע את הבלוק הרלוונטי לפי BULLET

## Slide 37: Image Manipulation Manager - µArchitucture
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 38: Img. Man. Manager - FSM
WBM
Biliniar
Addr_calc
WBS
Image Manipulation
registers
manager

## Slide 39: Banks managment
Division of the memory
explain

## Slide 40: Working methods
Top down design
Pipeline
Test bench
Results comparison with Matlab (Notepad++ plugin)
Components documenting
Synchronize files via SVN.
Notes: התכן נעשה על ידי בחינה של המערכת הכוללת, לאחר מכן תכן של הבלוק שלנו ואז בוצע תכן לכל רכיב בתוך הבלוק
האלגוריתם כולל חיושבים אריתמטיים עם הכפלות מרובות, והיות והכפלה הינה צרכן משאבים, פיצול החישוב משפר את הקצב התוצאות
בדיקת הרכיבים נעשתה על ידי יצירת קובץ TB לכל קומפוננטה, שמטרתו לדמות כניסות אפשריות למערכת ובדיקת התוצאות
בדיקת התוצאות נעשה מול האלגוריתם שרץ בסביבת MATLAB, השוואה עם פלט ויזואלי
תיעוד לאורך התהליך עזר בבננית המצגת, מסמך הפרויקט ולשימוש חוזר בעתיד
מאפשר עבודה מנקודות קצה שונות ושחזור במקרה של באגים

## Slide 41: Problems during the process (1)
Working with fractures
First version of addr_calc used fixed point package.
Problem occurred during synthesis.
Solution- work with regular std_logic_Vector, with relevant adjustments.

## Slide 42: Problems during the process (2)
Trigonometric calculations (sine, cosine)
planed to be executed by VHD process, consumes expensive hardware resources.
Solution- calculate Cos/Sin by software (Matlab).

## Slide 43: Problems during the process (3)
Timing issues- synthesis timing results did not meet the requirements.
solution- break arithmetic calculations into parts (piping).

## Slide 44: Problems during the process (4)
Architectural changes
In the original design, the top block included
addr_calc and addr_converter.
During the design, the 2 blocks were combined into one block seemed inevitable.
WBM
F
Biliniar
Addr
WBS
6
Image Manipulation
Param Reg
manager

## Slide 45: Conclusions/lessons (1)
Pipeline makes the throughput shorter. With “heavy” calculations, it is recommended to break the arithmetic process.

## Slide 46: Conclusions/lessons (2)
Working with generics parameters make the design more flexible.

## Slide 47: Conclusions/lessons (3)
Top down design divides the coding procedure into stages, allows more than one person to work on solution, allows parallel work.

## Slide 48: Missions ahead
Finish Image Man. Manager – complete read/write states
Complete Top Block
Integration with global system
Simulation of complete system
Synthesis- working with DE2

## Slide 49: Time Table – 2012-2013
Tasks | Month
Finish Image Man. Manager – complete read/write states | November
Complete Top Block, Integration with global system | December
Simulation of complete system | January
Synthesis- working with DE2 | February
Final Presentation – part B | March

## Slide 51
Flush
UART RX
MP Dec
RAM 1
SDRAM Controller
WBS
WBM – Wishbone Master
WBS – Wishbone Slave
Mem Ctrl Wr
Mem Ctrl Rd
SDRAM Arbiter
WBS
RAM 2
MP Enc
UART TX
WBM
WBM
WBS
INTERCON
FIFO
VESA
Ctrl.
req_ln_trig
& Pixels, VSync
Pixel Manager
(Req for Data)
WBM
MUX
Synthetic
Pic. Gen
WBS
1
2
3
A
E
5
D
Flush
Dual Clk FIFO
WBM
WBM
C
Z
wr_rd_bank
wr_cnt
wr_cnt_en
8 bit
8 bit
8 bit
8 bit
8 bit
8 bit
Hsync,
VSync
CheckSum
CheckSum
RX Path
TX Path
Display Controller
Memory
Management
WBS
4
INTERCON
Y
TYPE
Reg
Disp. Reg
Frame
Reg
TYPE Reg
DBG ADDR
Reg
INTERCON
X
Rd Burst Len
CRC ERR
EOF ERR
R1
B
R2
R1 – Ram 816 bits
R2 – Ram 168 bits
- 133 MHz
- 40 MHz
UART_SE
UART_PE
OR
Host
(Matlab)
VGA
Display
IS42S16400 SDRAM
DBG Command
WBM
Image Manipulation
Addr Calculator
Param Registers
WBS
WBM
TYPE
Reg
ImgMan Manger
RAM
ReadProc
WriteProc
Biliniar
Notes: לעדכן שרטוטים